Electricity Distribution Costs

Comparisons of Urban and Suburban Areas

Prepared by Paul Chernick and Patrick Mehr,
Lexington Electric Utility Committee
(10/28/03)

# Objective

A typical investor-owned utility (“IOU”) serves a large territory that includes urban areas and surrounding suburban (or even rural) areas. Each IOU charges the same rates to customers throughout its service territory, regardless of location. In discussions about the formation of new municipal electric utilities (“munis”), speculations have been advanced about the effect on cities if suburban towns municipalize and cease to be served by the IOU. If distribution costs are lower in suburban areas, and those communities depart, the IOU’s average costs, and hence its rates, will have to increase. If this “suburban flight” scenario were likely, and if distribution costs were lower in suburban areas, it would legitimately be a matter of considerable concern for city governments.

Whether municipalities will choose to form their own utilities will depend on many factors, including the municipality’s level of frustration with its IOU and the extent to which other issues preoccupy the municipal government. The critical factor in the suburban-flight scenario is the assumption that most suburban towns are less expensive to serve than most cities. Electricity distribution costs are driven by the type of infrastructure necessary to serve the local customer base. Certain features of the distribution infrastructure may, all other things equal, drive electricity distribution costs up or down. Specifically, compared to the suburbs, urban areas tend to have the following characteristics:

- A larger portion of the distribution infrastructure is underground, in vaults and conduit under streets and sidewalks, rather than overhead, on poles along streets.

- Construction and maintenance of the infrastructure is more difficult and expensive due to high building density, lack of room for setting up construction equipment, more congested streets, and higher real-estate costs for substations and other facilities.

- The load density is higher, that is, each mile of distribution circuit serves more customers and delivers greater amounts of electricity.

In urban areas, item (1) increases distribution investment (but reduces maintenance cost, since underground systems do not require tree-trimming and are less vulnerable to weather and accidents), item (2) tends to increase distribution costs, while item (3) tends to decrease costs, all compared to suburban areas. As the various characteristics of the distribution infrastructure drive costs in different directions, it is not clear whether electricity distribution costs would tend to be higher in urban or in suburban areas.

In principle, this question could be answered for the greater Boston area by computing Nstar’s cost of distribution service separately for urban and suburban areas. Such an analysis would require that Nstar track its investments and operating costs for each community it serves (or at least for groups of similar communities). So far as we know, Nstar has not tracked that information.

Absent the necessary cost information specific to the urban and suburban communities Nstar serves, this paper presents five alternative approaches to determining whether electricity distribution costs are generally higher in urban than in suburban areas.

# Comparisons: Data and Analysis

## Consolidated Edison’s Analysis of Urban and Suburban Costs

We are aware of only one published direct comparison of distribution costs in urban and suburban areas. In 1982, the staff of the New York Public Service Commission looked at the differences in costs between the two areas served by Consolidated Edison: New York City and Westchester. The study found that “A significant reason for the differences” in the cost of serving these areas was “the cost of the distribution system per unit of electricity sold... Although the underground system in New York City is expensive, the number of kWhs delivered per dollar of investment is very high. This means that expenses [are low] relative to revenues... Westchester, which is more suburban and rural in nature, has a low population density. This increases the unit costs.…”

In the study, Westchester was

- 11.8% of Consolidated Edison’s sales, but

- 12.6% of the peak load,

- 14.3% of distribution plant investment,

- 14.9% of services and meters investment, and

- 14.5% of distribution expenses.

This study suggests that the cost of distribution for New York City, the most urban of urban areas, is lower than the cost of providing service to its suburbs.

## Comparison of Rates for Nstar’s Subsidiaries

Nstar’s electric service territory consists of three subsidiaries:

- Cambridge Electric Lighting (CELCo): serves only Cambridge; totally urban, with a very high population density (about 30% higher than Boston’s).

- Boston Edison (BECo): serves the city of Boston, several smaller cities (e.g., Chelsea, Waltham) and the western suburbs; a mix of urban and suburban areas.

- Commonwealth Electric (CommElec): serves part of Southeastern Massachusetts and Cape Cod; mostly suburban (or even rural) areas, with a small urban area (New Bedford).

We compared Nstar’s residential rates for each of the three subsidiaries (from www.nstaronline.com), for customers with annual usage ranging from the average usage in Cambridge (400 kWh/month) to the average usage in the BECo and CommElec territories (about 600 kWh/month). Exhibit 1 shows the results of our comparison of both the “delivery” rates—all charges except supplier services (Nstar’s costs of purchasing power for its customers)—and distribution charges (just the customer and distribution charges).

Distribution costs for small, medium and large residential customers are the highest in Nstar’s least-urban area (Commonwealth Electric) and the lowest in Nstar’s most-urban area (Cambridge). Boston Edison distribution costs are in between, consistent with that service territory being a mix of urban and suburban areas.

Exhibit 1: Comparison of Nstar Company Residential Rates

|  |  | Cambridge Electric Light | Boston Edison | Commonwealth Electric |
| --- | --- | --- | --- | --- |
| Service territory |  | Cambridge only | Boston, suburbs | New Bedford, Plymouth, Cape Cod |
| Type of area |  | urban | mix urban, suburban | mostly suburban to rural |
| Customers per mile of line |  | 46 | 30 | 18 |
| % distribution underground |  | 71% | 34% | 20% |
| Rate (residential)* |  | 01 | A1 | 32—Annual |
| Delivery service charges* |  |  |  |  |
| Customer (per month) |  | $6.87 | $6.43 | $3.73 |
| Distribution (per kWh) |  | $0.02434 | $0.03900 | $0.04524 |
| Transition (per kWh) |  | $0.00308 | $0.01813 | $0.02717 |
| Transmission (per kWh) |  | $0.02366 | $0.00733 | $0.00534 |
| Energy Conservation (per kWh) |  | $0.00250 | $0.00250 | $0.00250 |
| Renewable Energy (per kWh) |  | $0.00050 | $0.00050 | $0.00050 |
| Delivery cost (¢/kWh) |  |  |
| 400 kWh/month customer |  | 7.1 | 8.4 | 9.0 |
| 600 kWh/month customer |  | 6.6 | 7.8 | 8.7 |
| Delivery cost (customer & distribution charges, ¢/kWh) |  |  |
| 400 kWh/month customer |  | 4.2 | 5.5 | 5.5 |
| 600 kWh/month customer |  | 3.6 | 5.0 | 5.1 |

## PEPCo’s Washington DC and Maryland Jurisdictions

We sought other examples, comparable to the Nstar situation, in which an urban utility is surrounded or adjacent to a suburban utility. We looked first at the most densely populated cities reported in the 2000 Census. Other than Cambridge, we did not find any cities served by an IOU that did not serve at least the suburbs, and often other cities and rural areas as well. Exhibit 2 summarizes the results for the highest-density cities.

Exhibit 2: Highest-Density Cities in US 2000 Census

| City | Population | Area (mi2) | Density (pop/mi2) | Utility | Serves |
| --- | --- | --- | --- | --- | --- |
| New York City, NY | 8,008,278 | 303.3 | 26404 | ConEd | NYC & Westchester |
| Paterson city, NJ | 149,222 | 8.4 | 17765 | PSE&G | big chunk northern NJ |
| San Francisco, CA | 776,733 | 46.7 | 16632 | PG&E | large & varied area |
| Jersey City, NJ | 240,055 | 14.9 | 16111 | PSE&G | big chunk northern NJ |
| Cambridge, MA | 101,355 | 6.4 | 15837 | CELCo | only Cambridge |
| Daly City, CA | 103,621 | 7.6 | 13634 | PG&E | large & varied area |
| Chicago, IL | 2,896,016 | 227.1 | 12752 | CommEd | Chicago & suburbs |
| Santa Ana, CA | 337,977 | 27.1 | 12471 | SCE | Serves cites, suburbs, rural |
| Inglewood, CA | 112,580 | 9.1 | 12371 | SCE | Serves cites, suburbs, rural |
| Boston, MA | 589,141 | 48.4 | 12172 | BECo | Boston & suburbs |
| El Monte, CA | 115,965 | 9.6 | 12080 | SCE | Serves cites, suburbs, rural |
| Hialeah, FL | 226,419 | 19.2 | 11793 | FP&L | most of FL |
| Newark, NJ | 273,546 | 23.8 | 11494 | PSE&G | big chunk northern NJ |
| Philadelphia, PA | 1,517,550 | 135.1 | 11233 | PECo | Philadelphia & suburbs |
| Yonkers, NY | 196,086 | 18.1 | 10833 | ConEd | NYC & Westchester |
| Norwalk, CA | 103,298 | 9.7 | 10649 | SCE | Serves cites, suburbs, rural |
| Miami, FL | 362,470 | 35.7 | 10153 | FP&L | most of FL |
| Elizabeth, NJ | 120,568 | 12.2 | 9883 | PSE&G | big chunk northern NJ |
| Berkeley, CA | 102,743 | 10.5 | 9785 | PG&E | large & varied area |
| Providence, RI | 173,618 | 18.5 | 9385 | Narragansett | most of RI |
| Washington, DC | 572,059 | 61.4 | 9317 | PEPCo | DC & MD suburbs |

None of these cities quite matches our criteria, but Washington comes close. While Potomac Electric Power (PEPCo) serves both Washington and the Maryland suburbs, DC and Maryland separately set rates for their areas, based on (among other things) the distribution investment and expenses in each jurisdiction. We obtained PEPCo’s basic residential rate schedules and other data by jurisdiction from PEPCo’s web site (www.pepco.com). As shown in Exhibit 3, the residential distribution rates for the urban part of the service territory are substantially lower than those for the suburban portion.

Exhibit 3: PEPCo Urban and Suburban Rates

| Service area |  | Washington DC | Maryland suburbs |
| --- | --- | --- | --- |
| Sq miles |  | 68 | 572 |
| Population served |  | 572,000 | 1,450,000 |
| Density (population/sq mile) |  | 8,412 | 2,535 |
| Type of area |  | urban | suburban |
|  |  | Summer | Winter | Summer | Winter |
| Residential rates: |  | (June-Oct) | (Nov-May) | (June-Oct) | (Nov-May) |
| Distribution service charge |  |  |  |  |  |
| Minimum charge, including first 30kWh ($/month) |  | $0.47 | $0.47 |  |  |
| kWh charge, next 370 kWh (¢/kWh) |  | 0.945 | 0.945 |  |  |
| kWh charge, in excess of 400 kWh (¢/kWh) |  | 2.845 | 1.942 |  |  |
| Customer ($ per month) |  |  |  | $5.54 | $5.54 |
| kWh charge, first 800 kWh (¢/kWh) |  |  |  | 3.112 | 1.953 |
| kWh charge, in excess of 800 kWh (¢/kWh) |  |  |  | 3.112 | 1.503 |
| Transmission service charge |  |  |  |  |  |
| Minimum charge, including first 30kWh ($/month) |  | $0.15 | $0.15 |  |  |
| kWh charge, in excess of 30 kWh (¢/kWh) |  | 0.521 | 0.521 |  |  |
| kWh charge, first 800 kWh (¢/kWh) |  |  |  | 0.514 | 0.514 |
| kWh charge, in excess of 800 kWh (¢/kWh) |  |  |  | 0.514 | 0.514 |
| Residential bill (855 kWh/month average, half in summer) (¢/kWh) |  |
| Distribution only |  | 1.74 | 3.17 |
| Distribution & transmission |  | 2.26 | 3.68 |

## Seattle and Environs

We also looked for suitable pairs involving large, but less dense, cities. Exhibit 4 lists those cities, down to populations of 300,000, or about half that of Boston. Most of these are not useful for our purposes, because the city is served by an IOU that also serves large surrounding suburban and rural areas (e.g., Houston, Phoenix, San Diego and Dallas), or because the city is served by a municipal utility, but the neighboring suburbs are served by an IOU with a mix of urban and suburban, and sometimes rural, loads (e.g., Sacramento, Austin, San Antonio). In southern California, both Los Angeles and several smaller nearby communities are served by separate munis, but the smaller cities are about as densely settled as Los Angeles (with comparable customers per mile of line and percentages of underground distribution), and are therefore not really good proxies for suburban towns in Massachusetts.

Exhibit 4: Largest Cities in 2000 Census

Excludes Cities in Exhibit 2.

| City | Population | Area (mi2) | Density (pop/mi2) | Utility |
| --- | --- | --- | --- | --- |
| Los Angeles, CA | 3,694,820 | 469.1 | 7876 | Muni |
| Houston, TX | 1,953,631 | 579.4 | 3372 |  |
| Phoenix, AZ | 1,321,045 | 474.9 | 2782 |  |
| San Diego, CA | 1,223,400 | 324.3 | 3772 |  |
| Dallas, TX | 1,188,580 | 342.5 | 3470 |  |
| San Antonio, TX | 1,144,646 | 407.6 | 2808 | Muni |
| Detroit, MI | 951,270 | 138.8 | 6854 |  |
| San Jose, CA | 894,943 | 174.9 | 5117 |  |
| Indianapolis, IN | 781,870 | 361.5 | 2163 |  |
| Jacksonville, FL | 735,617 | 757.7 | 971 | Muni |
| Columbus, OH | 711,470 | 210.3 | 3383 | CSP |
| Austin, TX | 656,562 | 251.5 | 2611 | Muni |
| Baltimore, MD | 651,154 | 80.8 | 8059 | BG&E |
| Memphis, TN | 650,100 | 279.3 | 2328 | Muni |
| Milwaukee, WI | 596,974 | 96.1 | 6212 |  |
| El Paso, TX | 563,662 | 249.1 | 2263 | El Paso Elec (also serves rural load) |
| Seattle, WA | 563,374 | 83.9 | 6715 | Muni |
| Denver, CO | 554,636 | 153.4 | 3616 | PSCo |
| Nashville-DavidsonTN | 545,524 | 473.3 | 1153 | Muni |
| Charlotte, NC | 540,828 | 242.3 | 2232 | Duke |
| Fort Worth, TX | 534,694 | 292.5 | 1828 |  |
| Portland, OR | 529,121 | 134.3 | 3940 | PacifiCorp & Portland General Electric |
| Oklahoma City, OK | 506,132 | 607 | 834 |  |
| Tucson, AZ | 486,699 | 194.7 | 2500 | APS |
| New Orleans, LA | 484,674 | 180.6 | 2684 | NOPSI |
| Las Vegas, NV | 478,434 | 113.3 | 4223 | NV Power |
| Cleveland, OH | 478,403 | 77.6 | 6165 | Muni & CEI |
| Long Beach, CA | 461,522 | 50.4 | 9157 | SCE |
| Albuquerque, NM | 448,607 | 180.6 | 2484 | PNM |
| Kansas City, MO | 441,545 | 313.5 | 1408 | KCP&L |
| Fresno, CA | 427,652 | 104.4 | 4096 |  |
| Virginia Beach, VA | 425,257 | 248.3 | 1713 |  |
| Atlanta, GA | 416,474 | 131.7 | 3162 |  |
| Sacramento, CA | 407,018 | 97.2 | 4187 | Muni |
| Oakland, CA | 399,484 | 56.1 | 7121 | PG&E |
| Mesa, AZ | 396,375 | 125 | 3171 |  |
| Tulsa, OK | 393,049 | 182.6 | 2153 |  |
| Omaha, NE | 390,007 | 115.7 | 3371 | Omaha PPD |
| Minneapolis, MN | 382,618 | 54.9 | 6969 |  |
| Colorado Springs, CO | 360,890 | 185.7 | 1943 | Muni |
| St. Louis, MO | 348,189 | 61.9 | 5625 |  |
| Wichita, KS | 344,284 | 135.8 | 2535 |  |
| Pittsburgh, PA | 334,563 | 55.6 | 6017 |  |
| Arlington, TX | 332,969 | 95.8 | 3476 |  |
| Cincinnati, OH | 331,285 | 78 | 4247 |  |
| Anaheim, CA | 328,014 | 48.9 | 6708 | Muni |
| Toledo, OH | 313,619 | 80.6 | 3891 |  |
| Tampa, FL | 303,447 | 112.1 | 2707 |  |

We considered Tennessee and Nebraska, because they are both served predominantly by publicly-owned utilities, which generally have smaller and more homogeneous territories. Nebraska did not turn out to be useful, because the public power districts serve large areas. For example, the largest Nebraska city, Omaha, is served by the Omaha Public Power District, which also serves 13 counties (and hence does not seem to be an urban utility). Tennessee provided more useful information, which we discuss in the next section.

Otherwise, the only example we found in the data was that of Seattle, which is served by a muni and has a total population and population density similar to Boston’s, while the neighboring Snohomish County (a largely suburban area) is served by a public utility district, which is essentially a special-purpose muni. As summarized in Exhibit 5, we computed the supply costs (purchased and generated power) for each of the utilities, and subtracted those supply costs from the residential and overall rates charged respectively by Seattle and Snohomish County to approximate their respective distribution costs (see Exhibit 3).

We found that distribution rates, as approximated in this analysis, were higher in suburban Snohomish County than in urban Seattle, both for residential customers and overall.

Exhibit 5: Comparison of Costs, Seattle and Vicinity

| Year 2001 | Source | Seattle Muni | Snohomish County PUD |
| --- | --- | --- | --- |
| Utility Name |  |  |  |
| Type of area |  | urban | suburban |
| Summer Peak (MW) | EIA-861 | 1,234 | 901 |
| Winter Peak (MW) | EIA-861 | 1,755 | 1,286 |
| Net Generation (MWh) | EIA-861 | 3,929,875 | 612,783 |
| Purch Util (MWh) | EIA-861 | 3,905,212 | 7,022,820 |
| Exchng-Net (MWh) | EIA-861 | 2,902,435 | -95,678 |
| Total Source (MWh) | EIA-861 | 10,617,126 | 7,539,925 |
| Sales to Consumers (MWh) | EIA-861 | 8,990,171 | 6,184,545 |
| Frnshd W/O Chrg (MWh) | EIA-861 | 78,740 |  |
| Total Production Expenses ($1,000) | EIA-412 | 403,151 | 369,121 |
| Total Production Plant ($1,000) | EIA-412 | 538,554 | 334,654 |
| Carrying Cost of Prodn plant (%/yr) | assumed | 5% | 5% |
| Cost of purchased & produced power, |  |  |  |
| net of resale revs (¢/kWh) | Lex EUC | 3.90 | 3.86 |
| Retail Revenue ($1,000) | EIA-861 | 503,437 | 395,501 |
| Resale Revenue ($1,000) | EIA-861 | 75,333 | 146,285 |
| Rates (by class of customer) minus wholesale power analysis |  |  |
| Residential Revenues ($1,000) | EIA-861 | 178,129 | 225,850 |
| Residential sales (MWh) | EIA-861 | 2,973,916 | 3,215,167 |
| Residential customers (#) | EIA-861 | 321,422 | 246,204 |
| MWh/year per residential customer |  | 9.3 | 13.1 |
| Residential rate (¢/kWh) |  | 5.99 | 7.02 |
| minus cost of power (¢/kWh) |  | 2.09 | 3.16 |
| Total Revenues ($1,000) | EIA-861 | 500,886 | 395,501 |
| Total sales (MWh) | EIA-861 | 8,974,215 | 6,184,545 |
| Total customers (#) | EIA-861 | 354,556 | 271,193 |
| Total rate (¢/kWh) | Lex EUC | 5.58 | 6.39 |
| minus cost of power net of resale revs (¢/kWh) | Lex EUC | 1.68 | 2.53 |

## Tennessee Municipal Utilities

There are 47 munis in Tennessee with more than 5,000 customers; each muni serves one or more cities, and typically some surrounding areas as well. All those munis purchase their wholesale electricity primarily from the Tennessee Valley Authority at similar prices. Therefore, differences in rates should be driven primarily by differences in distribution costs. Given this wealth of data, we decided to look at the effect of customer density on distribution costs (as reflected in rates) over the range of customer densities. We measured density as the ratio of the number of residential customers per mile of distribution circuit each muni serves. Exhibit 6 is our plot of the munis’ residential rates as a function of customers per mile of distribution circuits, including the linear trend line through the scatter plot.

Both the scatter plot and the trend line indicate that costs are lowest in the more urban service areas and increase as the service area becomes more suburban or rural.

Exhibit 6: Rates and Density of Tennessee Municipal Utilities

# Conclusions

All five analyses presented above are consistent with the conclusion that electricity distribution costs are lower in urban areas than in suburban areas.

- A full cost-allocation study with geographical accounting data for distribution costs found that distribution was less expensive in New York City than in its suburbs.

- Among the three Nstar subsidiaries, the least urban (CommElec) has the highest distribution rates, the most urban (Cambridge) has the lowest.

- The more urban portion of the PEPCo territory (Washington DC) has lower residential distribution rates than the suburban (Maryland) portion.

- Seattle City Light has lower delivery costs for residential customers and on average than the Snohomish PUD, which serves the surrounding suburban area.

- Among the Tennessee munis, all of which have essentially the same power supply, residential rates are lowest for the munis with the highest density of customers per mile of distribution circuits.

These analyses used all the viable approaches we could think of, short of performing a geographic cost-allocation study for BECo. They compare different parts of the same IOU, different IOUs owned by a holding company, and different publicly-owned utilities. They use an analysis by a regulatory agency, rate schedules, and accounting data. They use data from the 1980s, 1990s, and 2001, as well as current rates.

They all reach the same conclusion: The suburban-flight scenario rests on an assumption that is not only wrong, but backwards. If any group of municipalities have an economic incentive to form municipal electric utilities, it seems to be the large cities, not the suburbs.

Therefore, there is no reason to believe that making municipalization feasible in Massachusetts would disadvantage the larger cities, or force them to pay higher rates. To the contrary, an urban area such as Boston would benefit in three different ways from enactment of Bill H1468:

- By making practical the option to form a muni, Bill H1468 will create a form of competition for electricity distribution, thereby leading the IOU to provide better service and lower rates everywhere, including in urban areas.

- Just as for a suburban community, the economics of forming a muni for a city may turn out to be sufficiently attractive to warrant the effort, with possibly better service and substantial savings on their electricity bills for residents, businesses and the City itself.

- If a typical suburban town buys out its portion of the IOU’s infrastructure to form a new muni, the remainder of the IOU’s service territory, including the urban areas, will likely see a reduction in the IOU’s rates, since the IOU’s average distribution costs will decrease once the IOU no longer has to serve that high-cost suburb.

# Footnotes

Forty-one munis already exist in Massachusetts.

If municipalization simply allowed the communities with inherently lower costs to avoid the averaging of their costs with those of inherently more expensive communities, it might have little real benefit to the Commonwealth as a whole. A similar process, in which a competitor picks off the low-cost customers of a utility that is required to charge equal prices to all customers, is called “cherry-picking.” This is not a close parallel to municipalization, in which the “cherries” would be picking themselves, but the same terminology has been used by opponents of municipalization.

Quotes are from “A Study of the Comparative Costs of Electric Service in Westchester County and the City of New York,” Berak, F., Arnett, H., Nadel, J, New York Department of Public Service Power Division, Case 28157, January 29, 1982, pp. 4–5.

Commercial and industrial loads and customer mix vary more widely between utilities, and the rates for those customers are more complex, making comparisons of rates more difficult and less meaningful.

The Virginia suburbs are served by Virginia Power, which serves most of that state.

We actually looked at all US cities with a population of at least 100,000.

Nebraska utilities are all public; Tennessee has one small IOU.

We do not provide similar comparisons for commercial, industrial and “other” customers because those classes of customers are too varied.

We used data from the Utility Data Institute’s DarWin database for 1996.

We expect that inherent cost differences between communities are unlikely to drive municipalization. Some mix of low-cost and high-cost communities, urban, suburban and rural, may become seriously interested in municipalizing, depending on how dissatisfied they are with their IOU.